## Slide 1: Accel Mouse
P. Ahrendt, C. Siman-Chereches, S. Chenyu
Robotics Project

## Slide 2: Table of Contents
Introduction
The initial idea
Architecture
Implementation
Challenges
Prerequisite Libraries
The Final Design
Conclusion

## Slide 3: Introduction
Build a robotic application
Use sensors to estimate position or attitude of object
Our phones have the common sensors most robots use:
  Accelerometer
  Gyrometer
  Magnetometer

## Slide 4: The first try
Use the mouse on a flat surface, similar to how one would use a regular mouse
Assumption:
  Use our sensors to estimate delta x & y (change in position)
    Gyrometer and magnetometer don’t help for this
    So only Accelerometer is left
      Problem: sensor fusion is impossible, so no way to reduce noise
    Distance can be computed by double integration of acceleration
      Problem: due to noise there is a drift over time between the actual and estimated velocity
      Integrating the drifted velocity to get the position increases the drift exponentially

## Slide 5: Architecture

## Slide 6: Architecture
Measure inertia with internal sensors
Mouse gets moved on the monitor
Send estimated angle and other events
1
2
3
Receive and process data further
Send calculated mouse position, clicks
and key press events

## Slide 7: Architecture - Server
Handles the incoming data
Maps pitch and yaw attitude to pixels of display
Controls the mouse through a Python shell on MacOS and JavaScript shell on Windows
Applies a Kalmann filter (for 1D data) to the final displacement to reduce noise

## Slide 8: Architecture - Estimation of Euler angles
Swift library to get the accelerometer, magnetometer and gyrometer data
Estimate pitch and roll from accelerometer data:
Pure accelerometer estimate yielded better results than when combined with gyrometer data

## Slide 9: Architecture - Estimation of Euler angles
Estimate yaw from gyroscope and magnetometer
Complementary for final yaw estimate

## Slide 12: Code implementation

## Slide 13: The IIR Filter
Objective: We need to filter the output noise of the accelerometer.
The filter we use:
The calculation of coefficients using MATLAB:

## Slide 14: The IIR Filter
The code of the filter
data.json The data to send
sendtoserver.py sends data to server every ms
The IIR filter in the server serverreception.js
output.json the output result
the data.json and output.json in MATLAB

## Slide 15: Challenges

## Slide 16: iPhone sensory data
Axes of the IMU vectors are configured differently
There is separate raw data for the calibrated and uncalibrated magnetometer output
4

## Slide 17: Data transmission
Asynchronously sending data introduces problems:
  Sometimes data is received in the wrong order
  Differing packet number sent in a period
  Sending data fast enough will throttle the received packets
A websocket allows for two-way low-latency communication
Other times, you just forget a hard-coded 3 second delay in your package sending script. Oops!

## Slide 18: Magnetic North
The yaw angle is in the range [-π,π] but when you go above π, the angle resets to -π
  This happens due to the position of the magnetic north and has to be accounted for in the yaw calculation
While testing the app, the environment was mostly not facing magnetic north, so the error case was difficult to notice
The solution was to add/subtract 2π each time the angle was switching

## Slide 19: Noisy or unreliable projection
Phone orientation vector is projected onto the screen
A complementary filter and a 1D Kalmann filter is required
Mapping from can be too sensitive

## Slide 20: Prerequisite Libraries
General
  Mathjs – math qol functions, better than native js
  Websocket – for websocket communication
  Kalmanjs – simple Kalman noise filter for 1D data
On MacOS
  Pyautogui – mouse, keyboard events, screen info
On Windows
  Node-cursor – for easier mouse driver access
  VS 2019 and Windows C++ Dev. Kit – for accessing drivers
  Robotjs – for sending keyboard events, reading screeninfo

## Slide 21: Final Design
Switching windows, scrolling, and even presenting is possible with the phone
Data processing can happen on the server, or on the phone depending on demand
A usable, universally available mouse pointer

## Slide 22: Conclusion
Phone attitude estimation using the in-built sensors can be used to control a cursor or possibly a robot
Using a complementary filter with the accelero-, magneto-, and gyro-meter yields a robust attitude estimation

## Slide 23
Pointing at things with your phone is...
FUN

## Slide 24: References
https://media.istockphoto.com/vectors/desktop-computer-icon-vector-isolated-vector-id942286504?k=20&m=942286504&s=170667a&w=0&h=faK8_FvtXDV0rGQh43k3SfCzFfBs7HgccQwWFw8j9Mg=
https://www.clipartmax.com/png/middle/277-2772015_iphone-clipart-smartphone-accessory-celular-sin-fondo-png.png
https://www.clipartmax.com/png/middle/4-42693_server-clip-art-server-clipart.png
https://docs-assets.developer.apple.com/published/1c3e1a60a4/10421a93-a1dd-41a8-a9c0-7147d3f47f27.png
https://github.com/callmechristian/mouse-server
https://github.com/phiahr/accel_mouse
Robotics Lecture

## Slide 25: Thank you!
Questions?